## Slide 1
1
2
Notes: On opening HM the User Profiles screen will appear. This changes what you can and cant use on the menus below. For FEA stuff always choose Abaqus Standard 3D.
To open a file click the Open folder (1), or to import from Avizo , click the green arrow (2)

## Slide 2
Notes: The menu at bottom right (highlighted in red box) is the way to access all the different tools needed. Unless otherwise mentioned the 2D, 3D, Analysis, Tool functions are all here

## Slide 3
Notes: To change the order of elements, go to 2D > order change (last column, 3rd from bottom). Hold down the shift key + left click drag over the elements. Make sure change to 1st is selected and click change order. Press return

## Slide 4
Notes: Go to Tool > Check elems (F10). Click duplicates (none will be found, but follow the steps anyway as they will be useful for later editing e.g. aspect ratios and min/max angles). Then save failed. Press return.

## Slide 5
Notes: On the Tool panel, you will find a delete button (2nd column, 3rd down. Alternatively press F2). This brings up the screen shown. Click on the elems box (blue highlight) to bring up a new screen (next slide). If the elems is not visible, click the down arrow on the left and select elems from the list

## Slide 6
Notes: Click retrieve to return the saved elements. You can also select many things in many of the menus using this method. If there are any failed elements, they should highlight upon retrieval and the original delete screen should return. Press delete entity.

## Slide 7
Notes: Press return on the delete screen to get back to the main menus list. Now it is time for intersections/penetration checks. Click Tool > penetration (4th column, bottom)

## Slide 8
Notes: This screen appears. Make sure the comps is selected (blue highlight box. Select from dropdown if elems is preselected. Doesn’t really make any difference, just saves the shift+left click drag to select all). Click the box to include self interference

## Slide 9
Notes: This should appear. Press check.

## Slide 10
Notes: This check will take a while, and often it will say Not Responding at the top. Just give it time (up to 10 minutes depending on the complexity of the model). If you click back on the hypermesh window during this time, it will probably go white as above. Just give it time.

## Slide 11
RESULTS ^
Notes: A new tab appears with your results listed. Click the Intersections (1) to reveal the number of failed/intersected triangles.

## Slide 12
Notes: To view the failed elements click the two buttons near the top of the tab (arrows). Zoom in on the area highlighted in red (ctrl + mouse wheel)

## Slide 13
Notes: You are now viewing some failed elements. It may not be obviously clear what the problem is so you need to view the surrounding triangles. Click Unmask adjacent (red arrow, or hover over the panels to see what they are).

## Slide 14
Notes: This should appear. It is still not obvious what the problem is…

## Slide 15
Notes: Simplest way to deal with these issues is to delete the problems and rebuild them. To do this, Tool > delete (F2 – as before). Click on all of the light blue elements and press delete. 5 entities will delete, but 2 more remain… Problem? I think this might be it.

## Slide 16
Notes: Delete those last 2 elements too.

## Slide 17
Notes: Now we need to repair the holes. Go to 2D > edit element

## Slide 18
Notes: This panel (a very useful one for editing elements, hence the name) appears. From here you are able to create, merge or split elements easily. To fix the current problem, make sure create and tria are selected. Click the corner nodes where you want your triangle to build (in above example just need to click the left node to build the triangle).

## Slide 19
Notes: Repeat for the remaining triangles until your model appears something like this. If you mess up, right click to undo a build or on highlighted nodes to deselect them.

## Slide 20
Notes: Scroll across the screen (right click drag), until you find this area of failed elements.

## Slide 21
Notes: Go the delete panel (Tool > delete or F2 – last time of telling) and delete the big lighter blue element that goes across the screen.

## Slide 22
Notes: Now you want to recheck the model to make sure you’ve fixed those ones. Click the tick box (red arrow. Hover over to show names)

## Slide 23
Notes: Click Yes

## Slide 24
Notes: It often fails… but it will get you back to the penetration tab rapidly. Click on one of the elements again, and click check.

## Slide 25
Notes: Again click Intersection (1) to reveal the number of failed elements, then the two buttons to show just them. Attempt to autofix these failed elements by clicking the little wrench at bottom left (small red arrow)

## Slide 26
Notes: You can see the new little yellow wrench appears by the number of failed elements (top left arrow) and you should see that some of the elements are no longer obviously intersected (big arrow, middle of screen)

## Slide 27
Notes: Recheck again and display the failed ones again. You can see there are only a few left that are still intersected. You can either autofix these again, or manually correct the error (recommended in this case and a useful tool to use)

## Slide 28
Notes: Unmask adjacent once and rotate the area (ctrl+left click drag). To change point of rotation ctrl+left click node. Here you can see that the two layers have collapsed onto each other.

## Slide 29
Notes: Unmask adjacent again to see how far the collapsed area extends.

## Slide 30
Notes: Deselect the failed and select the highlight failed elements (next to the review failed elements). You will need to unmask adjacent again to expose everything again, but it will make it clearer for the next bit. Then go to 2D > element offset (2nd column, bottom). Make sure shell offset is selected, then click on the elements at the lowest point of the collapse (as above).

## Slide 31
Notes: A problem with the offset is it is not always clear if you want an offset + or an offset - . Try one and if it makes it worse, reject and press the other. Also note the distance is in whatever ambiguous measure HM wants. Often its in mm/cm depending on the scaling of your model. If unsure, just go to Geom > distance and click 2 nodes on a triangle to give you a rough idea of how big each is.

## Slide 32
Notes: Feel free to rotate the model and look if it has fixed the problem. I think it needs another offset of roughly the same amount. Highlight elements and repeat

## Slide 33
Notes: It now looks relatively normal from above, rotate and check the side

## Slide 34
Notes: Looks good! Recheck penetrations

## Slide 35
Notes: Now time to check t-connections. Tool > edges (4th column, 2nd from top or Shift+F3). It reveals this screen. Click the up/down arrow next to free edges. This will change to t-connections. Click on the skull and press find edges. Some number of edges will be found.

## Slide 36
Notes: The easiest way to display them is to close the penetrations tab (click the button marked by red arrow)

## Slide 37
Notes: Click Yes

## Slide 38
Notes: Make sure you are on the Model tab. Here you will see a new material called “^edges” has appeared. These are your t-connections.

## Slide 39
Notes: Click the little mesh looking square next to the “Solidskull136” material so it goes see-through. This should leave only the ^edges visible (read t-connections)

## Slide 40
Notes: As with the penetrations, click unmask adjacent to show the surrounding elements. Zoom in on the highlighted area.

## Slide 41
Notes: Delete the entity in the middle (F2). Repeat until none in the middle

## Slide 42
Notes: Then rebuild the element (F6) as before.

## Slide 43
Notes: Now to hide the ones you’ve fixed, go to Tool > mask (2nd column, 2nd down or F5).

## Slide 44
Notes: Shift + left click drag over the elements and release

## Slide 45
Notes: This highlights them all. Press mask.

## Slide 46
Notes: These elements are now hidden

## Slide 47
Notes: Find the next failed one (this is a good one). Just delete the silly element, and then mask the remaining elements as above

## Slide 48
Notes: Just these 2 left. Zoom in on the right hand one

## Slide 49
Notes: Here you can see what appears to be one error

## Slide 50
Notes: If you rotate you can see that the 2 layers have stuck themselves to each other.

## Slide 51
Notes: Easiest way is to delete those surrounding the join

## Slide 52
Notes: Half done

## Slide 53
Notes: Repeat on other side

## Slide 54
Notes: Then rebuild the triangles in

## Slide 55
Notes: Et voila. Fixed. Mask the elements and find the last errors

## Slide 56
Notes: I leave this one up to you, although Id suggest deleting elements and rebuilding, but be sure to keep the finished geometry as close as possible to the original

## Slide 57
Notes: When finished, go back to the edges panel (Shift+F3), click on the model, and press find edges again.

## Slide 58
Notes: Hopefully your result is this… no t connections found and the ^edges component disappears

## Slide 59
Notes: Time to check free edges. Press the up/down arrow to change it from t-connections back to free edges. Click on the model again, and then click find edges.

## Slide 60
Notes: As with t-connections, a new component appears again. Hide the solidskull component again by clicking the little box to the right of it.

## Slide 61
Notes: Then click unmask adjacent to show the problems with the surrounding elements. Zoom in on the right side failure

## Slide 62
Notes: Its just a hole… build a new element in. Then mask it.

## Slide 63
Notes: Go find this set. At first glance there appears to be nothing wrong…

## Slide 64
Notes: Zoom in to see the nodes have separated from each other

## Slide 65
Notes: Go to 2D > replace. Click one node (a grey or white blob will appear), then the other.

## Slide 66
Notes: This should zip that section up as it combines the 2 nodes.

## Slide 67
Notes: Repeat on the other sections. NB there is sometimes an easier way to fix things like that. There is a Tolerance area showing 0.010 presently. If you click equivalence this will zip together all nodes that are within that distance of each other but not connected. Can be useful for minor gaps like this, but can be a pain as they tend to stick narrow areas together. Experience will tell you which is the best way to deal with things.
When finished, click on the find edges again to make sure no more edges have been found.

## Slide 68
Notes: Now time to check dihedrals. If following Jen’s guide you can skip step 4 as it wont apply. Click the Utility tab (top left), then Geom/Mesh

## Slide 69
Notes: Then click Quick Tetramesh

## Slide 70
Notes: Click on the Components button. It might take 2 goes to get to the next screen

## Slide 71
Notes: Click comps

## Slide 72
Notes: Tick the box and press select

## Slide 73
Notes: Click proceed

## Slide 74
Notes: Then click Dihedrals. It will reveal these ones. Zoom in on the main one in the centre of the square

## Slide 75
Notes: It looks like this. There are 2 types of dihedrals: tight angles and wide angles. This is an example of a wide angle. Basically they will normally be triangles with nothing apparently wrong with them

## Slide 76
Notes: To find out what is wrong with them, go to Tool > Normals (Shift+F10). Make sure comps is selected and click on the mesh again, and click the up down arrow next to Vector display normals. Change this to Colour display normals and hit display normals

## Slide 77
Notes: Now you can see the issue. Elements have an “inside” (red) and an “outside” (blue). Sometimes elements get confused which way around they are supposed to be or you build them in backwards. Fret not as its an easy fix.

## Slide 78
Notes: Click the orientation elem and then click an element on screen that is the “correct” way around. The click adjust normals. You can always reverse normals if they are backwards when you unmask all.

## Slide 79
Notes: They are now all the same!

## Slide 80
Notes: Recheck the dihedrals again, and only this one should appear.

## Slide 81
Notes: If you rotate you can see its not the same as the others. This is a “tight” angle. One where the elements on each side of the node are within 30 degrees of each other

## Slide 82
Notes: Depending on the circumstance you can either 2D > elem offset; merge the nodes with the 2D > replace; or delete and rebuild. I chose to replace the nodes, but this was personal preference

## Slide 83
Notes: When finished recheck and fix until this appears after a recheck.

## Slide 84
Notes: Time to do element quality checks. Go to Tool > Check elems (same place as duplicates also F10). First up is aspect ratio. Ideally all will be below 5, but up to 10 is often acceptable. Don’t get lazy if there aren’t many to fix though… As before, click Aspect then Save failed.

## Slide 85
Notes: I like to keep them intact, but you could delete them as with duplicates and then go back to edges and check for free edges, and fix them as needed. Go to Tool > mask. Click elems

## Slide 86
Notes: Retrieve.

## Slide 87
Notes: mask

## Slide 88
Notes: reverse

## Slide 89
Notes: These are the 76 that failed. Zoom in, unmask adjacent, and fix as with other errors. Repeat this cycle for min angle (again ideally 20, but can go as low as 10), and max angle (>150).

## Slide 90
Notes: To create new components for the tetrameshing, follow above and then give it a name (tetmeshed for example). NB NO NUMBERS AS ABAQUS DOESN’T LIKE THEM

## Slide 91
Notes: Make sure it is current by right clicking and pressing make current (it will be listed in bold). Then click 3D > tetramesh

## Slide 92
Notes: Click Tetramesh parameters, then select gradual.

## Slide 93
Notes: Make sure it says comps in the blue box and click the skull somewhere. Then click mesh.

## Slide 94
Notes: This can take a while depending on the machine and size of the model. When it finishes it will list the number of elements in the bottom left.

## Slide 95
Notes: To create a new material, click the Materials area (red arrow – Folder with a hourglass under a bell curve?)

## Slide 96
Notes: Enter a mat name, select type = MATERIAL and card image = ABAQUS_MATERIAL. Then click create/edit

## Slide 97
Notes: Scroll down and click Elastic then enter your Youngs modulus (E1) and Poisson ratio (NU 1). Click return.
NBMake sure you have everything scaled correctly for this bit! TO check go to Geom > Distance and pick to points a known distance apart and see how big it is. Use 2D > scale to get it to the correct size in nm/mm/cm/m etc.

## Slide 98
Notes: Then click Properties (folder with a grey square on it, next to the materials).

## Slide 99
Notes: Enter a property name, type = SOLID SECTION, Card image = SOLIDSECTION, Material = (whatever you named your material). Click create

## Slide 100
Notes: Then go to assign. Shift + left click drag over all elements, then click assign.